## Slide 1
Circuit 1: Low Current
GND
2.048V ref (LM4040)
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
100 ohm
MCP3421 I2C (16 bit resolution)
x4 or x 8
Arduino Uno I2C

## Slide 2
Circuit 2: 65.6 mA through divider
GND
3.3V from Arduino Uno
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
50 ohm
MCP3421 I2C (16 bit resolution)
x 8
Arduino Uno I2C

## Slide 3
Circuit 3: 65.5 mA through Divider
GND
3.3V 800mA Linear Voltage Regulator - LD1117-3.3 TO-220
w/ in and out 10 uF electrolytic caps for stability
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
50 ohm
MCP3421 I2C (16 bit resolution)
x 8
Arduino Uno I2C

## Slide 4
Circuit 4: 65.5 mA through Divider
GND
3.3V 800mA Linear Voltage Regulator - LD1117-3.3 TO-220
w/ in and out 10 uF electrolytic caps for stability
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
50 ohm (2 precision 100 ohm in parallel)
- Would sometimes have to change this resistance to avoid clipping on ADC
MCP3421 I2C (16 bit resolution)
Arduino Uno I2C
GND
x 76
x 2
2.048V ref (LM4040)
~1.99V to 5.87V
75kohm/1kohm

## Slide 5: New Proposed Circuits for Final PCB Design
Reducing Current, Increasing Accuracy and Sampling Rates

## Slide 6
GND
ADS115 I2C (12 bit resolution for 800SPS)
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
Circuit V1 Option -> 13.07 mA + n x 12mA for additional sensors
Circuit Component | Current Draw (mA)
Divider Circuit (LT3092) | ~ 12 mA
MAX6070 | ~ 0.2 mA
LMC6482 | ~ 0.6 mA
ADS115 or MCP3421 (16 bit) | ~ 0.22 mA
INA333 | ~0.05 mA
x50
2.048V ref MAX6070 (or 2.048V LM4040)
x1
RP2040
-0.896 to 1.4V (out of possible -2.048 V to 2.048V)
x240
2.048V ref MAX6070 (or 2.048V LM4040)
ina333
1.152 V –3.456V
(4mV – 11.59 mV)
2.048V ref (through LMC6482 as a follower)
LT3092 12mA current source
(And 0.833 ohm external resistor)
(4.8mV – 14.4 mV) + 2.048V

## Slide 7
LT3092 12mA current source
(And 0.833 ohm external resistor)
GND
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
Circuit V2 Option -> 22.8 mA + n x 12mA for additional sensors
Circuit Component | Current Draw (mA)
Divider Circuit (LT3042 ) for each sensor | 12 mA
MAX6070 | ~ 0.2 mA
LMC6482 | ~ 0.6 mA
ADS131M02 (or 8 channel) | ~ 10 mA
(4.8mV – 14.4 mV) + 2.048V
RP2040 SPI Interface
2.048V ref (through LMC6482 as a follower)
x128 PGA
2.048V ref MAX6070 (or 2.048V LM4040)
ADS131M02 (SPI)
2-channel (up to 8 available) 24-bit, 64-kSPS
(-16mV to 16mv allowed and I would be using: 4.8mV – 14.4 mV)