## Slide 1: Kinematic Presentation Tom
5/19/25

## Slide 2
Completed:
Velcro testing on length samples
  Different way of plotting train one sample and apply model on reapplied and misaligned samples
Testing Current Source Circuit. Provides INCREDIBLY LOW NOISE DATA. Will use for PCB design but not for camera design to keep circuit consistent with bench top testing
Circuit design for 4 strain sensors
Order Camera equipment
  Begin programming python code for data acquisition

## Slide 3
Length Data Tested Using Velcro

## Slide 4
Reapplication Data Tested Using Velcro

## Slide 5
Misalignment Data Tested Using Velcro

## Slide 6
Plan was to finish making different cross-sectional area liquid metal channels today to test tomorrow: 0.017”x 0.017”, 0.02”x 0.02”, and 0.023” x 0.023”
  0.01”x 0.01”, 0.02”x 0.02”, and 0.03” x 0.03”
Test new delta sigma ADC 24 bit with 128x gain possible using SPI communication protocol. If works, can use this for the PCB design since one chip can take up to 8 sensors and sampling frequency up to kHz range.
  This board not needed for camera testing, just for final pcb design potentially
Order Camera equipment
  Begin programming python code for data acquisition
To Do:

## Slide 7
GND
MCP3421 I2C (16 bit resolution)
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
Circuit V1 Option -> 7.5 mA
Circuit Component | Current Draw (mA)
Divider Circuit (LT3092) | ~ 7.5 mA
MAX6070 | ~ 0.2 mA
LMC6482 | ~ 0.6 mA
ADS115 or MCP3421 (16 bit) | ~ 0.22 mA
INA333 | ~0.05 mA
x50
2.048V ref MAX6070 (or 2.048V LM4040)
x2
Arduino
x831
GND
OPA333
1.152 V –3.456V
(4mV – 11.59 mV)
LT3092 7.5mA current source
(75K:100 ohm resistor ratio)
Practically no noise at rest!

## Slide 8
Theoretical Model vs. Channel Cross-Section

## Slide 9
Circuit 5 for Camera Setup: 65 mA through each divider (can be adjusted to 15mA)
GND
ADM7150 3.3V 800 mA
75 ohm
Strain Gauge (0.4 ohm – 1.2 ohm)
75 ohm
75 ohm
75 ohm
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
GND
GND
GND
GND
X76 (LMC6482 or OPA333)
2.048V
2.048V
ADS115 I2C (two unique addresses 0x48, 0x49)
x 2
x 2
2.048V
2.048V
2.048V ref (LM4040 or MAX6070)
IMU
IMU
(two unique addresses, 0x28, 0x29)
Rasberry Pi
I2C
Circuit 5 for Camera Setup: same circuit has bench top testing with exception what ADC is ADS115, not MCP3421, to handle the higher sampling frequency at 16 bit -> 200-500 Hz