## Slide 1: Kinematic Presentation Tom
5/19/25

## Slide 2
Completed:
Velcro testing on length samples
  Different way of plotting train one sample and apply model on reapplied and misaligned samples
Testing Current Source Circuit. Provides INCREDIBLY LOW NOISE DATA. Will use for PCB design but not for camera design to keep circuit consistent with bench top testing
Circuit design for 4 strain sensors
Order Camera equipment
  Begin programming python code for data acquisition

## Slide 3
Length Data Tested Using Velcro

## Slide 4
Reapplication Data Tested Using Velcro

## Slide 5
Misalignment Data Tested Using Velcro

## Slide 6
Plan was to finish making different cross-sectional area liquid metal channels today to test tomorrow: 0.017”x 0.017”, 0.02”x 0.02”, and 0.023” x 0.023”
  0.01”x 0.01”, 0.02”x 0.02”, and 0.03” x 0.03”
Test new delta sigma ADC 24 bit with 128x gain possible using SPI communication protocol. If works, can use this for the PCB design since one chip can take up to 8 sensors and sampling frequency up to kHz range.
  This board not needed for camera testing, just for final pcb design potentially
Order Camera equipment
  Begin programming python code for data acquisition
To Do:

## Slide 7
GND
MCP3421 I2C (16 bit resolution)
GND
Strain Gauge (0.4 ohm – 1.2 ohm)
Circuit V1 Option -> 7.5 mA
Circuit Component | Current Draw (mA)
Divider Circuit (LT3092) | ~ 7.5 mA
MAX6070 | ~ 0.2 mA
LMC6482 | ~ 0.6 mA
ADS115 or MCP3421 (16 bit) | ~ 0.22 mA
INA333 | ~0.05 mA
x50
2.048V ref MAX6070 (or 2.048V LM4040)
x2
Arduino
x831
GND
OPA333
1.152 V –3.456V
(4mV – 11.59 mV)
LT3092 7.5mA current source
(75K:100 ohm resistor ratio)
Practically no noise at rest!

## Slide 8
Theoretical Model vs. Channel Cross-Section

## Slide 9: Model vs. Data for Different Cross-Sections

## Slide 10
Circuit 5 for Camera Setup: 65 mA through each divider (can be adjusted to 15mA)
GND
ADM7150 3.3V 800 mA
75 ohm
Strain Gauge (0.4 ohm – 1.2 ohm)
75 ohm
75 ohm
75 ohm
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
GND
GND
GND
GND
X76 (LMC6482 or OPA333)
2.048V
2.048V
ADS115 I2C (two unique addresses 0x48, 0x49)
x 2
x 2
2.048V
2.048V
2.048V ref (LM4040 or MAX6070)
IMU
IMU
(two unique addresses, 0x28, 0x29)
Rasberry Pi
I2C
Circuit 5 for Camera Setup: same circuit has bench top testing with exception what ADC is ADS115, not MCP3421, to handle the higher sampling frequency at 16 bit -> 200-500 Hz

## Slide 11
Circuit PCB for PCB Differential Setup: Option 1
GND
LT3092
(Current Source)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
GND
GND
GND
GND
X76 (LMC6482 or OPA333)
2.048V
2.048V
ADS115 I2C (two unique addresses 0x48, 0x49)
x 2
x 2
2.048V
2.048V
2.048V ref (LM4040 or MAX6070)
IMU
IMU
(two unique addresses, 0x28, 0x29)
Rasberry Pi
I2C
7.5 mA
7.5 mA
7.5 mA
7.5 mA

## Slide 12: Evaluating Different ADC’s For Final PCB Design
ADC | Single, Diff, or Both | PGA | Bit Resolution | SPS (max) | Communication | OpAmp? Ref V? | ADC Clipping?
ADS115 | Both | 16 | 16 | 820 | I2C | Yes, No | Yes if Differential
AD7140 | Both | 128 | 24 | 19.2K | SPI | No, No | No
MCP3564 | Both | 128 | 24 | 152K | SPI | No, No | No

## Slide 13
Circuit PCB for PCB: Option 2 Single Ended ADC (No Resistor Dividers, Opamps, or Volt Ref)
GND
LT3092
(Current Source)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
GND
GND
GND
GND
AD7124 SPI (8 single ended channels)
x 128
IMU
IMU
(two unique addresses, 0x28, 0x29)
RP2040
GND
4x Analog in
7.5 mA
7.5 mA
7.5 mA
7.5 mA

## Slide 14: 6/18/25: AD7124-4 Working: Try diff mode next time!
Ch0
Ch1
Ch2
Ch3
Ch4
GND
AD7124-4
ESP-WROOM-32
(3.3V)
3.3V ref in from ESP 3.3V pin
(LM4040 2.048V didn’t work??)
100 ohm
100 ohm
470 ohm
470 ohm

## Slide 15
GND
6.2 V supply

## Slide 16: 7/7/25: Completed or In Progress
4 strain gauge board with 4 current sources done
Stream 4 independent strain gauge data via Arduino and spi and ad7124 adc done
Rasberry Pi flash new OS Kuiper Linux done
  Connect to adc via Rpi and python in progress
Installed SpinMaker SDK on windows for camera capture streaming done
  Need dedicated usb 3 splitter and power supply to run both cameras simultaneously waiting for usb 3 hub to arrive today
Successfully ran Preeya Single Camera capture python code done
  Run dual camera python code In progress
  Triggering single camera withRPI GPIO in progress (conceptually very simple and clear)

## Slide 17: 7/14/25: Completed or In Progress
4 strain gauge board with 4 current sources done
Stream 4 independent strain gauge data via Arduino and spi and ad7124 adc done
Rasberry Pi flash new OS Kuiper Linux done
  Connect to adc via Rpi and python done
Installed SpinMaker SDK on windows for camera capture streaming done
  Need dedicated usb 3 splitter and power supply to run both cameras simultaneously done
Successfully ran Preeya double Camera capture python code in progress
  Run dual camera python code In progress
  Triggering each camera withRPI GPIO done

## Slide 18: Data as DataFrame -> CSV

## Slide 19
Circuit PCB for PCB: Option 2 Single Ended ADC (No Resistor Dividers, Opamps, or Volt Ref)
3.3V
LT3092 x 4
(Current Source)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
Strain Gauge (0.4 ohm – 1.2 ohm)
GND
GND
GND
GND
AD7124-8 SPI (8 single ended channels)
4x OPA333 x Gain??
7.5 mA
7.5 mA
7.5 mA
7.5 mA
4x Analog in
MAX6070 Prec. Volt Ref. 2.048V
SPI Output to Arduino